## Slide 1
Lowering the environmental impact of infrastructures with efficient design of low carbon footprint steel solutions
June 16th 2022
Dr.-Ing Oliver Hechler
Dipl.-Ing. João Martins
Dr.-Ing. Mike Tibolt
Dr.-Ing. Dennis Rademacher
***Changing imagery*** 1 Right click on the image and select ‘Change picture’ 2 Choose your replacement 3 Use the crop tool to scale and position within the shape

## Slide 2: The climate emergency
Jun.
Berlin, London, NYC, Paris, Venice,…
Extinction Rebellion demonstrations
Dec
Nov
COP21. Paris Agreement.
Pursue efforts to limit the temperature increase to 1.5°C above pre-industrial levels
RICS, UK standards.
Whole life carbon
assessment for the built environment
Greta Thunberg:
“I don’t want your hope. I want you to panic. I want you to act.
I want you to act as if our house is on fire.”
2015
Apr.
2017
2018
2019
2020
2022
Nov.
Pictures: https://www.unep.org/explore-topics/climate-action/facts-about-climate-emergency; Christophe Petit Tesson/European Pressphoto Agency; https://www.theguardian.com/environment/2019/jan/25/our-house-is-on-fire-greta-thunberg16-urges-leaders-to-act-on-climate; https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.france24.com%2Fen%2Fvideo%2F20190701-extinction-rebellion-civil-disobedience-direct-action&psig=AOvVaw3wk1ltopbpiHW2SyUnpoV-&ust=1631044904370000&source=images&cd=vfe&ved=2ahUKEwiBvq_ykevyAhVR8BQKHWwlC1oQjRx6BAgAEAk; https://builtenvironmentdeclares.com/
Dec
50% of Australia’s Great Barrier Reef already died across the globe since 1995 due to warmer seas driven by climate change
Page 2
Mosty 2022
16/06/2022

## Slide 3: Climate emergency is a driver to decarbonise the construction market (38% of global CO2-emissions in 2019 *)
By 2030, all new buildings, infrastructure and renovations will have at least 40% less embodied carbon with significant upfront carbon reduction, and all new buildings must be net zero operational carbon.
By 2050, new buildings, infrastructure and renovations will have net zero embodied carbon, and all buildings, including existing buildings, must be net zero operational carbon.
World Green Building Council
Extract from Bringing embodied carbon upfront
“
“
* United Nations Organization: 2020 GLOBAL STATUS REPORT FOR BUILDINGS AND CONSTRUCTION
Page 3
Mosty 2022
16/06/2022
Page 3

## Slide 4: The climate emergency … and our commitment to be net zero by 2050
May
Jun.
Berlin, London, NYC, Paris, Venice,…
Extinction Rebellion demonstrations
Dec
Nov
net zero2050
CO2 ↓ 30% by 2030 ArcelorMittal Europe
COP21. Paris Agreement.
Pursue efforts to limit the temperature increase to 1.5°C above pre-industrial levels
RICS, UK standards.
Whole life carbon
assessment for the built environment
Greta Thunberg:
“I don’t want your hope. I want you to panic. I want you to act.
I want you to act as if our house is on fire.”
Jun.
ArcelorMittal Europe
Climate Action Report
ArcelorMittal
Climate Action report #1
ArcelorMittal Climate Action Report #2 CO2 ↓35% by 2030 in Europe
2015
Apr.
Nov
2017
2018
2019
2020
2021
Nov.
Pictures: https://www.unep.org/explore-topics/climate-action/facts-about-climate-emergency; Christophe Petit Tesson/European Pressphoto Agency; https://www.theguardian.com/environment/2019/jan/25/our-house-is-on-fire-greta-thunberg16-urges-leaders-to-act-on-climate; https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.france24.com%2Fen%2Fvideo%2F20190701-extinction-rebellion-civil-disobedience-direct-action&psig=AOvVaw3wk1ltopbpiHW2SyUnpoV-&ust=1631044904370000&source=images&cd=vfe&ved=2ahUKEwiBvq_ykevyAhVR8BQKHWwlC1oQjRx6BAgAEAk; https://builtenvironmentdeclares.com/
Dec
Jun.
Jul
50% of Australia’s Great Barrier Reef already died across the globe since 1995 due to warmer seas driven by climate change
Page 4
Mosty 2022
16/06/2022

## Slide 5: ArcelorMittal has a clear ambition to decarbonise its production
May 2019:
First group climate action report
July 2021:
Second group climate action report
May 2020:
European climate action report
Plans to become net-zero by 2050
September 2020:
December 2019:
ArcelorMittal’s ambition to significantly reduce CO2 emissions globally and become carbon-neutral in Europe by 2050.
  ArcelorMittal Europe sets target to cut carbon emissions by 30% by 2030
2030 global carbon emissions intensity reduction target of 25%
European 2030 carbon emissions intensity reduction target increased to 35% from 30% previously announced.
  ArcelorMittal sets 2050 net-zero target
Page 5
Mosty 2022
16/06/2022

## Slide 6: With XCarb® products, our customers benefit directly from our investments
XCarb® recycled and renewably produced steel is made in the EAF using both scrap and certified renewable energy, enabling it to reach very low levels of embodied CO2e
We intend to develop our portfolio of XCarb® products to enable customers to take advantage of all our efforts to decarbonise as we progress towards our net zero by 2050 target
XCarb® green steel certificates represent real savings in our CO2 emissions through targeted investment that can be attached to steel shipments, enabling customers to report a reduction in their Scope 3 carbon emissions
TODAY, XCarb® has been created:
To meet the demand from customers
To take advantage of ArcelorMittal’s existing decarbonisation investments
OVER TIME
Page 6
Mosty 2022
16/06/2022

## Slide 7
(1) World steel Association, Climate change and the production of iron and steel, 2021
XCarb® recycled and renewably produced steel has a far smaller carbon footprint than steel produced on the primary route (BF/BOF)
The average for the global steel industry is around 1.85 tonnes of CO2-eq emissions per tonne of steel products.(1)
Up to 100%
recycled scrap
100%
renewable electricity
Page 7
Mosty 2022
16/06/2022

## Slide 8: Green(er) Steel with low carbon footprint
1990
2000
2004
2015
2020
2016
2018
2021
2011
AZ range
S 355 GP
High strength grades S430GP & S460AP
AZ-700 large / lighter sheet piles
AMLoCor grade for maritime applications
AZ-800 extra large / extra light sheet piles
EPD (Environmental Product Declaration)
EPD EcoSheetPile
100%recycled (EAF)
EPD EcoSheetPile NL
“Cradle To Cradle” certification
EPD EcoSheetPile Plus
Mass
(kg/m²)
Co2-eq / t
Innovation
Innovation
100.0
82.6
78.4
72.2
937
520
429
370

## Slide 9
© Abako
New train station in Varberg, Sweden
1,200 t PU 22 and AZ 44-700N

## Slide 10
GWP* at: 370 kg CO2/t steel
Fishing terminal in the Egersund port in Norway
EcoSheetPile™ Plus
Sections
The longest pedestrian bridge in Europe between Esch and Belval, in Luxembourg
GWP* at: 333 kg CO2/t steel
Bars and rods
First trial order in XCarb®
Hjulsbro, in Sweden.
Pre-Constrained strands producer.
Final application: railway sleepers
GWP* at: 300 kg CO2/t steel

## Slide 11: The structural engineer has more opportunity to reduce carbon emissions than most other people
Cut one return flight to New York in economy
Cut meat, dairy and beer from your diet
Stop driving your car
20% structural embodied carbon reduction achieved (*)
Save 1,000 kgCO2e
Save 2,000 kgCO2e
Save 3,000 kgCO2e
Save 200,000 kgCO2e
The climate emergency is a driver to reduce the carbon footprint of our everyday lives…
… and even more for the structural engineer
Actions to reduce carbon footprint
16/06/2022

## Slide 12: How to come from product level to reduce the carbon footprint of specific projects ?
Environmental impacts are assessed  Life Cycle Analysis (LCA)
  It encompasses the extraction of all the raw materials and their further processing, the transport, the manufacturing of the product, any additional processing before installation at the jobsite, the use phase, the dismantlement and finally the reuse or recycling of the product
An EPD is a weighted average of the environmental footprint of a product based on its diverse applications
  It is the result of several LCAs of a single product
Independent study by KIT comparing steel/steel composite solutions with concrete solutions
  Focus on environmental aspects and external costs (03/2021)
Case study 1: Varying substructure
Case study 2: Varying superstructure
D. Rademacher, A. Barceló, O. Hechler: Life-cycle and External Cost Assessment for Bridges with Small and Medium Spans. 25. MEZINÁRODNÍ SYMPOZIUM MOSTY/BRIDGES 2020. Brno, 2020.

## Slide 13: National economy costs
Deviation
Page 13
Mosty 2022
16/06/2022
D. Rademacher, A. Barceló, O. Hechler: Life-cycle and External Cost Assessment for Bridges with Small and Medium Spans. 25. MEZINÁRODNÍ SYMPOZIUM MOSTY/BRIDGES 2020. Brno, 2020.

## Slide 14: Case study 1 Varying substructure
Option 1:
Sheet pile abutment
Sheet pile length of 16 m (abutment) and 13 m (wing walls)
Option 2:
Reinforced concrete abutment with concrete piles
Piles =0,9m and L=10 m
2 piles per wing wall and 4 piles per abutment
22,5 m
22,5 m
11,5 m width superstructure
Page 14
Mosty 2022
16/06/2022
D. Rademacher, A. Barceló, O. Hechler: Life-cycle and External Cost Assessment for Bridges with Small and Medium Spans. 25. MEZINÁRODNÍ SYMPOZIUM MOSTY/BRIDGES 2020. Brno, 2020.

## Slide 15: Case study 1: Costs Varying substructure
Chart: 
| Autobahn unten | Landesstraße oben
Herstellung | 1980770.7793 | 2234329.436
Nutzung | 1109702.375 | 1072478.1293
Rückbau | 488892.5382 | 268119.5323
Construction costs
Life-cycle costs
External costs
Equipment
Superstructure
Substructure
Temporary / Planning
DTV 70.000 Veh./day, 3-lane motorway
2% real discount rate
Chart: 
| Autobahn unten | Landesstraße oben
Herstellung | 1553962.1735 | 1876836.7262
Nutzung | 1109702.375 | 1072478.1293
Rückbau | 488892.5382 | 178746.3549
Chart: 
| Stb.-Wdl.
Unterbau | 336120.864
Überbau | 239997.328
Ausbau | 163565.392
Temporär & Planung | 302050
Chart: 
| Spundwand-Wdl.
Unterbau | 281458.7952
Überbau | 239997.328
Ausbau | 163565.392
Temporär & Planung | 283900
Chart: Years
+8%
+8%
+5%
+13,5%
+14,3%
+27%
SSP abutments
RC abutments
RiWiBrü modified
Steel sheet pile abutment
Reinforced concrete abutment
Motorway below
Country road on top
Motorway below
Country road on top
Construction
Operation
Dismantling
16/06/2022
D. Rademacher, A. Barceló, O. Hechler: Life-cycle and External Cost Assessment for Bridges with Small and Medium Spans. 25. MEZINÁRODNÍ SYMPOZIUM MOSTY/BRIDGES 2020. Brno, 2020.

## Slide 16
Global warming potential by member group
+1%
+1%
Stahlverbund-Überbau
Chart: 
 | 4.3973 | 5.7726 | 0.026122 | 0.0041859 | 0.13243 | 0.41513 | -0.0087054 | -0.0044319 | 4.5472 | 6.1875
 | 2.6333 | 2.6333 | 0.45818 | 0.45818 | 0.11695 | 0.11695 | -0.12697 | -0.12697 | 3.0815 | 3.0815
 | 2.1709 | 2.1709 | 4.258 | 4.258 | 0.063698 | 0.063698 | -0.15187 | -0.15187 | 6.3407 | 6.3407
ges.
0,31
ges.
0,60
Equipment
Superstructure
Substructure
gesamt
ges.
-0,29
ges.
-0,28
Transport:
Steel beams/sheet piles: 500 km truck
Concrete: 50 km truck
+12%
Sheet pile
abutment
Reinforced concrete abutment
Data sets used:
Sheet piles : EPD EcoSheetPiles
Concrete C20/25 - C30/37: ökobau.dat
+36%
+31%
Functional unit: m² bridge area per year
GWP [kg CO2-eq./(m²∙year)]
Production
(A1-5)
Operation
(B1-7)
Dismantling
(C1-4)
Recycling D
Total
Reinforcing steel: ökobau.dat
Corrosion protection: NaBrü-research project (GaBi data sets)
Case study 1: LCA
Varying substructure
16/06/2022

## Slide 17: Case study 2 Varying superstructure
Variant 1:
Steel composite deck (S460)
Variant 3:
Prestressed concrete (in-situ)
Single span bridge with steel sheet pile abutments
Plan view
Traffic area
Traffic direction 1
Traffic direction 2
Traffic direction 1
Traffic direction 2
Page 17
Mosty 2022
16/06/2022
D. Rademacher, A. Barceló, O. Hechler: Life-cycle and External Cost Assessment for Bridges with Small and Medium Spans. 25. MEZINÁRODNÍ SYMPOZIUM MOSTY/BRIDGES 2020. Brno, 2020.

## Slide 18: Case study 2: Costs Varying superstructure
Chart: 
| Autobahn unten | Landesstraße oben
Herstellung | 1553962.1735 | 1429970.839
Nutzung | 1109702.375 | 1072478.1293
Rückbau | 488892.5382 | 178746.3549
Chart: 
| Autobahn unten | Landesstraße oben
Herstellung | 3046001.3663 | 2144956.2585
Nutzung | 768255.4904 | 1072478.1293
Rückbau | 488892.5382 | 178746.3549
Chart: Years
Chart: 
Unterbau | 254170.607
Überbau | 255275.7012
Ausbau | 163655.692
Temporär | 335200
Chart: 
Unterbau | 254170.607
Überbau | 293067.8016
Ausbau | 163655.692
Temporär & Planung | 283900
Construction costs
Life-cycle costs
External costs
Equipment
Superstructure
Substructure
Temporary / Planning
+1%
+1%
+37%
+27%
+96%
-2%
DTV 70.000 Veh./day, 3-lane motorway
2% real discount rate
Steel composite deck
Prestressed concrete deck
Motorway below
Country road on top
Motorway below
Country road on top
Steel composite deck
Prestressed concrete deck
Construction
Operation
Dismantling
16/06/2022
D. Rademacher, A. Barceló, O. Hechler: Life-cycle and External Cost Assessment for Bridges with Small and Medium Spans. 25. MEZINÁRODNÍ SYMPOZIUM MOSTY/BRIDGES 2020. Brno, 2020.

## Slide 19
+1%
+1%
Stahlverbund-Überbau
Chart: 
Unterbau | 3.9979 | 3.9979 | 0.025861 | 0.025861 | 0.062194 | 0.062194 | -0.013908 | -0.0086608 | 4.072 | 4.0773
Überbau | 2.8971 | 3.4776 | 0.40925 | 0.37656 | 0.15125 | 0.22086 | 0.14908 | -0.015954 | 3.6066 | 4.0591
Ausstattung | 2.171 | 2.171 | 4.2586 | 4.2586 | 0.063723 | 0.063723 | -0.15187 | -0.15187 | 6.3415 | 6.3415
Chart: 
A1-3 | 3.0811
A4 | 0.11252
A5 | 0.30811
ges.
0,28
ges.
0,35
A 4 Transport (0,08)
ges.
-0,02
ges.
-0,18
A 5 Erection (0,26)
A1-3 Product manufacturing (2,56)
+3%
Data sets used:
Steel sections HISTAR: EPD
Concrete C20/25 - C30/37: ökobau.dat
Reinforcing steel: ökobau.dat
Corrosion protection: NaBrü-research project (GaBi data sets)
Transport:
Steel girders / sheet piles
500 km truck
Concrete
50 km truck
Global warming potential by member group
Functional unit: m² bridge area per year
Equipment
Superstructure
Substructure
Steel-composite
beams
GWP [kg CO2-eq./(m²∙year)]
Prestressed concrete beams
Production
(A1-5)
Operation
(B1-7)
Dismantling
(C1-4)
Recycling D
Total
Renewal corrosion protection steel girders
+12%
+20%
Case study 2: LCA Varying superstructure
Page 19
Mosty 2022
16/06/2022

## Slide 20: How to value these efforts by construction industry ?
Green credentials should be considered in public tenders
Prime example: Netherlands
  Systematic enforcement of environmental criteria in a scheme for public tenders that lead to the most sustainable solution, based on the most economically advantageous tender
  Use of the monetization scheme, which is based on a weighting method applied to multiple environmental indicators either from national EPDs or from generic data contained in a national database
  The calculated overall ECI (Environmental Cost Indicator) comprises the quantities of the materials having a large repercussion on the environmental footprint of the project and is converted into a financial credit that is subtracted from the overall price.
  Thus, the contract is not necessarily awarded to the contractor with the lowest bid (price)
6,67 M€
8,0 M€

## Slide 21: Summary and conclusions
Greenhouse gases to be reduced  infrastructure projects
ArcelorMittal has launched XCarb® to lower the environmental impacts of products / projects
A holistic approach for infrastructures is essential  Life Cycle Analysis (LCA)
LCA example “bridge foundation”:
  External costs: -12 %
  GWP (modules A1-A5): - 13 %
LCA example “bridge superstructure”:
  External costs: -24 %
  GWP (modules A1-A5): - 6 %
Further potential with XCarb® recycled and renewably produced steel: - 30-35 % (A1-A3)
Effort to reduce the carbon footprint must be valued in tendering

## Slide 22: Thanks for your attention and let’s stay connected !